## Slide 1: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 14: Serial Communications in C
14.3 Inter-Integrated Circuit (I2C) Bus – What is it and Why the Pull-up Resistors?

## Slide 2: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.1 The I2C Protocol
The Inter-Integrated Circuit (I2C) standard is a serial interface implement with a two-wire link that can support multiple masters and multiple slaves.

## Slide 3: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.1 The I2C Protocol
The Inter-Integrated Circuit (I2C) standard is a serial interface implement with a two-wire link that can support multiple masters and multiple slaves.
Providing a clock allows higher data rates over UART.

## Slide 4: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.1 The I2C Protocol
The Inter-Integrated Circuit (I2C) standard is a serial interface implement with a two-wire link that can support multiple masters and multiple slaves.
Providing a clock allows higher data rates over UART.
The two-wire interface allows devices to be added without increasing the number of lines like on SPI.

## Slide 5: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.1 The I2C Protocol
An I2C bus contains a clock line (SCK) and data line (SDA).

## Slide 6: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.1 The I2C Protocol
An I2C link is always half-duplex, meaning that all devices share the data line with only one device transmitting at any given time.

## Slide 7: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.1 The I2C Protocol
Open-drain output stage – supports multiple drivers on the same signal line using NMOS transistor.

## Slide 8: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.1 The I2C Protocol
NMOS Transistor Operation

## Slide 9: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.1 The I2C Protocol
NMOS Transistor Operation
  The NMOS switch will turn ON and close when its gate voltage is at VCC.

## Slide 10: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.1 The I2C Protocol
NMOS Transistor Operation
  The NMOS switch will turn ON and close when its gate voltage is at VCC.
  When the NMOS is ON, a conduction path is formed between its other two terminals, which effectively closes the switch.

## Slide 11: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.1 The I2C Protocol
NMOS Transistor Operation
  The NMOS switch will turn ON and close when its gate voltage is at VCC.
  When the NMOS is ON, a conduction path is formed between its other two terminals, which effectively closes the switch.
  The NMOS will switch OFF when the gate voltage is at GND.

## Slide 12: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.1 The I2C Protocol
NMOS Transistor Operation
  The NMOS switch will turn ON and close when its gate voltage is at VCC.
  When the NMOS is ON, a conduction path is formed between its other two terminals, which effectively closes the switch.
  The NMOS will switch OFF when the gate voltage is at GND.
  When the NMOS is OFF, there is no conduction path between the source and drain, which effectively opens the switch.

## Slide 13: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.1 The I2C Protocol
Consider the Open-Drain Output Stage:

## Slide 14: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.1 The I2C Protocol
Consider the Open-Drain Output Stage:
  If we turn on the NMOS by driving a HIGH (1) to its gate, it will pull the I2C line to GND, or LOW (0).
HIGH (1)
LOW (0)
ON

## Slide 15: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.1 The I2C Protocol
Consider the Open-Drain Output Stage:
  If we turn off the NMOS by driving a LOW (0) to its gate, the line is left floating, which is an unknown logic level.
LOW (0)
???
OFF

## Slide 16: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.1 The I2C Protocol
Consider the Open-Drain Output Stage:
  If we turn off the NMOS by driving a LOW (0) to its gate, the line is left floating, which is an unknown logic level.
  If a pull-up resistor it placed on the line, it will pull the resistor to a HIGH (1) when the NMOS is off.
LOW (0)
HIGH (1)
OFF

## Slide 17: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.1 The I2C Protocol
Consider the Open-Drain Output Stage:
  But now we have an inverted logic scheme where: - Driving a LOW to the NMOS yields a HIGH on the line. - Driving a HIGH on the NMOR yields a LOW on the line.

## Slide 18: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.1 The I2C Protocol
Consider the Open-Drain Output Stage:
  But now we have an inverted logic scheme where: - Driving a LOW to the NMOS yields a HIGH on the line. - Driving a HIGH on the NMOR yields a LOW on the line.
  To get back to positive logic, we insert an inverter before the NMOS.

## Slide 19: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.1 The I2C Protocol
Consider the Open-Drain Output Stage:
  But now we have an inverted logic scheme where: - Driving a LOW to the NMOS yields a HIGH on the line. - Driving a HIGH on the NMOR yields a LOW on the line.
  To get back to positive logic, we insert an inverter before the NMOS.
LOW (0)
ON
HIGH
LOW (0)

## Slide 20: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.1 The I2C Protocol
Consider the Open-Drain Output Stage:
  But now we have an inverted logic scheme where: - Driving a LOW to the NMOS yields a HIGH on the line. - Driving a HIGH on the NMOR yields a LOW on the line.
  To get back to positive logic, we insert an inverter before the NMOS.
HIGH (1)
OFF
LOW
HIGH (1)

## Slide 21: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.1 The I2C Protocol
An I2C bus ALWAYS needs external pull-up resistors on each of its lines.
These can’t be implemented on the MCU because the resistor function is only available when the port is configured as an INPUT.
Since I2C is bidirectional, we never know wither the pin will be an input or output.

## Slide 22: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 14: Serial Communications in C
14.3 Inter-Integrated Circuit (I2C) Bus – What is it and Why the Pull-up Resistors?
www.youtube.com/c/DigitalLogicProgramming_LaMeres

## Slide 23: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 14: Serial Communications in C
14.3 Inter-Integrated Circuit (I2C) Bus – Basic Packet Structure

## Slide 24: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.1 The I2C Protocol
Master – the device that initiates communication and controls the clock.
Multiple masters are also supported on an I2C bus.

## Slide 25: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.1 The I2C Protocol
Slave – a device on the bus that is read or written to, but does not initiate transmission or provide a clock.
Slave address – a unique and predetermined address for each slave on the bus.
This address is used by the master to indicate which slave it wants to communicate with.

## Slide 26: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.1 The I2C Protocol
Idle – when both SDA and SCL are held high by the pull-up resistors and no I2C device is attempting to communicate.
Busy – when devices are driving the bus.
Messages – how I2C information is transferred.

## Slide 27: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.1 The I2C Protocol
A master initiates a new message by generating a START (S) condition by pulling SDA LOW while SCL is still HIGH.
As soon as the START condition is generated, the SCL will be pulled LOW and start pulsing to provide the clock for the message.

## Slide 28: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.1 The I2C Protocol
The master is responsible for pulsing the clock.

## Slide 29: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.1 The I2C Protocol
Each clock pulse within the I2C message is numbered by periods.
Both the master and the slaves count the number of periods that have occurred since the message started in order to know when certain frames and signals should be present.

## Slide 30: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.1 The I2C Protocol
After the master generates the START condition, it first sends the slave address that it wishes to communicate with.
I2C slave addresses can either be 7-bit (default) or 10-bit.

## Slide 31: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.1 The I2C Protocol
The slave address is followed by the read/write signal indicating which type of transaction is being requested in the message.
The START condition, slave address, and read/write signal constitute periods 1 → 8.

## Slide 32: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.1 The I2C Protocol
Period 9 of the message is reserved for the slave acknowledge (ACK) or no-acknowledge (NACK) signal.
After the slave address and read/write signal are sent by the master, each slave on the bus checks whether it is being addressed.

## Slide 33: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.1 The I2C Protocol
If a slave exists with the specified slave address, it will send an ACK signal back to the master by pulling SDA LOW.
If no device exists with the specified slave address, no device will pull down SDA. This will result in period 9 remaining HIGH and will be interpreted as a NACK.

## Slide 34: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.1 The I2C Protocol
If the master sees the ACK signal, it knows a slave exists with the specified address and proceeds with the message.

## Slide 35: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.1 The I2C Protocol
After each byte is sent, the receiving device sends an ACK signal indicating that it successfully received the data.

## Slide 36: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.1 The I2C Protocol
A STOP condition occurs when there is a LOW-to-HIGH transition on SDA while SCL is HIGH.
Once, SDA goes HIGH, SCL also remains HIGH indicating that the bus is idle again.

## Slide 37: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.1 The I2C Protocol
A NACK in period 9 tells the master that no slave exists with the specified address.
The master then generates a STOP condition and ends the message.
NACK

## Slide 38: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.1 The I2C Protocol

## Slide 39: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.1 The I2C Protocol
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
When the master is writing to a slave, the master sends the 8-bits of data and the slave produces the ACK/NACK signal.
When the master is reading from a slave, the slave sends the 8-bits of data and the master produces the ACK/NACK signal.
After the data has been sent and acknowledged, the master can end the message by generating the STOP condition anytime.
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 40: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.1 The I2C Protocol
The Master can send multiple data bytes in a single message.

## Slide 41: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 14: Serial Communications in C
14.3 Inter-Integrated Circuit (I2C) Bus – Basic Packet Structure
www.youtube.com/c/DigitalLogicProgramming_LaMeres

## Slide 42: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 14: Serial Communications in C
14.3 Inter-Integrated Circuit (I2C) Bus – Addressing Slave Registers

## Slide 43: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.1 The I2C Protocol
Review of the Basic I2C Message Structure

## Slide 44: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.1 The I2C Protocol
I2C devices contain individual registers that hold their information.
In the simplest case, an I2C device contains only a single register.

## Slide 45: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.1 The I2C Protocol
Writing to a slave with a single register.
  The master initiates the message by sending the S bit.
  The master provides the slave address and a WRITE signal.
  The slave ACKs to indicate it is ready.
  The master writes the data.
  The slave sends an ACK that it got the data.
  The master ends the message by sending the P bit.
No register address is needed.

## Slide 46: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.1 The I2C Protocol
Reading from a slave with a single register.
  The master initiates the message by sending the S bit.
  The master provides the slave address and a WRITE signal.
  The slave ACKs to indicate it is ready.
  The slave sends the data.
  The master sends a NACK to stop the slave from sending more data.
  The master ends the message by sending the P bit.
No register address is needed.

## Slide 47: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.1 The I2C Protocol
When an I2C device has multiple registers, each is assigned a register address.
To access a specific register in the slave, the master needs to provide the register address in the message.

## Slide 48: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.1 The I2C Protocol
For a write transaction, the master generates an I2C message that first provides the slave address, then provides the register address to access, then provides the data to be written.
After each frame, the slave sends an ACK signal.

## Slide 49: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.1 The I2C Protocol
The master can also write a block of data to registers.
The slave automatically increments the starting address after each byte of data is written.
The master still sends the slave address, the write signal, and the starting register address.
The next byte of data that is sent goes into the first register address location.

## Slide 50: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.1 The I2C Protocol
The slave will continue to increment its register address until it sees the STOP condition generated by the master.
Check the slave’s datasheet for details!!!

## Slide 51: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.1 The I2C Protocol
When reading from a device that contains multiple registers, two message are needed.

## Slide 52: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.1 The I2C Protocol
When reading from a device that contains multiple registers, two message are needed.
The first message sets the register address within the slave that will be read from using a write transaction.
The first message puts the slave into a mode where it’s expecting a second message that will read data from the register address that was just sent.

## Slide 53: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.1 The I2C Protocol
The second message performs a read transaction that retrieves the data from the register address sent in the first message.

## Slide 54: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.1 The I2C Protocol
An alternative approach can also be used where a second START (Sr) condition is generated before the STOP condition of the first message.
This initiates the second read transaction immediately without giving up control of the bus.

## Slide 55: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.1 The I2C Protocol
The master can also read blocks of data from a slave.
In this situation, the master still sends two messages, the first setting the register address and the second retrieving the data.
In the second message, the master continually sends SCL pulses to read as many bytes as it wants prior to generating the STOP condition.

## Slide 56: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.1 The I2C Protocol
A repeated Start bit (Sr) can also be used to read blocks of information.

## Slide 57: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 14: Serial Communications in C
14.3 Inter-Integrated Circuit (I2C) Bus – Addressing Slave Registers
www.youtube.com/c/DigitalLogicProgramming_LaMeres

## Slide 58: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 14: Serial Communications in C
14.3 Inter-Integrated Circuit (I2C) Bus – Master Operation on the MSP430FR2355

## Slide 59: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.1 The I2C Protocol
The MSP430FR2355 contains two eUSCIs that support I2C – eUSCI_B0 and eUSCI_B1.
These two eUSCI peripherals are configurable to either support I2C or SPI.

## Slide 60: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.1 The I2C Protocol
eUSCI_B0 has SCL and SDA signals that share pins with ports on the MCU - port 1, bits 3 and 2 respectively.
Each eUSCI_B1 has SCL and SDA signals that share pins with ports on the MCU - port 4, bits 7 and 6 respectively.

## Slide 61: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.1 The I2C Protocol
The PxSEL1: PxSEL0 registers are used to select which serial peripheral drives the pins on the MSP430FR2355 MCU.

## Slide 62: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.2 I2C Master Operation on the MSP430FR2355
The I2C system contains a variety of configuration registers that are used to trigger events, indicate when certain conditions have occurred, and hold various information such as the slave address and the data sent or received.

## Slide 63: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.2 I2C Master Operation on the MSP430FR2355
• eUSCI_Bx Control Word 0 (UCBxCTLW0) – has different bit fields when in I2C mode.
• eUSCI_Bx Control Word 1 (UCBxCTLW0) – has different bit fields when in I2C mode.
• eUSCI_Bx Bit Rate Control Word (UCBxBRW) – same function as in SPI mode.
• eUSCI_Bx Status (UCBxSTATW) – has different bit fields when in I2C mode.
• eUSCI_Bx Byte Counter Threshold (UCBxTBCNT)
• eUSCI_Bx Receive Buffer (UCBxRXBUF) – same function as in SPI mode.
• eUSCI_Bx Transmit Buffer (UCBxTXBUF) – same function as in SPI mode.
• eUSCI_Bx I2C Own Address 0 (UCBxI2COA0)
• eUSCI_Bx I2C Own Address 1 (UCBxI2COA1)
• eUSCI_Bx I2C Own Address 2 (UCBxI2COA2)
• eUSCI_Bx I2C Own Address 3 (UCBxI2COA3)
• eUSCI_Bx Received Address (UCBxADDRX)
• eUSCI_Bx Address Mask (UCBxADDMASK)
• eUSCI_Bx I2C Slave Address (UCBxI2CSA)
• eUSCI_Bx Interrupt Enable (UCBxIE) – has different bit fields when in I2C mode.
• eUSCI_Bx Interrupt Flag (UCBxIFG) – has different bit fields when in I2C mode.
• eUSCI_Bx Interrupt Vector (UCBxIV) – has different bit fields when in I2C mode.

## Slide 64: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.2 I2C Master Operation on the MSP430FR2355
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Step 1: Set the UCSWRST bit in the UCBxCTLW0 configuration register to put the eUSCI_Bx peripheral in to software reset.
Step 2: Initialize all the eUSCI_Bx configuration registers.
Step 3: Configure ports.
Step 4: Clear UCSWRST – takes the eUSCI_Bx out of reset.
Step 5: Enable interrupts (optional) in the UCBxIE configuration register.
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 65: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.2 I2C Master Operation on the MSP430FR2355
The clock setup is the same as SPI.
UCSSEL chooses between an external pin, ACLK, or SMCLK.
The UCBxBRW register holds the prescalar value used to divide down the clock.

## Slide 66: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.2 I2C Master Operation on the MSP430FR2355
The slave address is stored in the UCBxI2CSA register.
This value is automatically shifted out first after a Start bit.

## Slide 67: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.2 I2C Master Operation on the MSP430FR2355
14.3.2.1 Writing Data as an I2C Master

## Slide 68: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.2 I2C Master Operation on the MSP430FR2355
The R/W! signal is configured in UCBxCTLW0. It is automatically sent out after the slave address.

## Slide 69: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.2 I2C Master Operation on the MSP430FR2355
The I2C state machine watches for the slave address ACK signal before proceeding.

## Slide 70: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.2 I2C Master Operation on the MSP430FR2355
Data is then either written or read.
To write, data is stored in the Tx Buffer prior to triggering the message Start bit.
To read, data is available in the Rx buffer after it arrives.

## Slide 71: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.2 I2C Master Operation on the MSP430FR2355
A “Byte Counter” is used to control how many bytes of data will be read or written in a message.
The byte counter is held in register UCBxTBCNT.

## Slide 72: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.2 I2C Master Operation on the MSP430FR2355
14.3.2.1
Writing Data
as an I2C
Master
Needed for minimal setup.

## Slide 73: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.2 I2C Master Operation on the MSP430FR2355
14.3.2.1
Writing Data
as an I2C
Master
Needed for minimal setup.
Needed for minimal setup.
This is how a message is started

## Slide 74: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.2 I2C Master Operation on the MSP430FR2355
14.3.2.1 Writing Data as an I2C Master
The next step is selecting the clock for the eUSCI_Bx peripheral.
When in I2C model, the default setting for UCSSELx = 11, which selects SMCLK on the MSP430FR2355.
The only other choices for BRCLK is the external pin UCBxCLK (UCSSELx = 00).
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 75: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.2 I2C Master Operation on the MSP430FR2355
14.3.2.1 Writing Data as an I2C Master
The next step to set up the clock is configuring the UCBxBRW register, which is the prescaler/divider for the source clock.
The value that is stored into UCBxBRW will divide the incoming clock source to produce the SCL that will be used by the master and all slaves.
This register is used in the same way for the I2C as in SPI as a clock prescaler/divider.
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 76: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.2 I2C Master Operation on the MSP430FR2355
14.3.2.1 Writing Data as an I2C Master
The UCMODEx bits dictate whether the peripheral is set up in SPI or I2C (UCMODEx = 11 for I2C).
Since only SPI and I2C are used in the eUSCI_Bx peripherals, the synchronous mode enable (UCSYNC) bit is always high.
The UCMST bit in UCBxCTLW0 dictates whether the MCU will be the I2C master (UCMST = 1) or slave (UCMST = 0).
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 77: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.2 I2C Master Operation on the MSP430FR2355
14.3.2.1 Writing Data as an I2C Master
The UCTR bit dictates whether the MCU will be transmitting (UCTR = 1) or receiving (UCTR = 0) data.
The UCA10 bit configures whether the MCUs own slave address is 7-bits or 10-bits when the MCU is the slave.
The UCA10SLA bit configures whether the external slave address is 7-bits or 10-bits when the MCU is the master.
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 78: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.2 I2C Master Operation on the MSP430FR2355
14.3.2.1 Writing Data as an I2C Master
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
There are also four bits within UCBxCLTW0 that will trigger events on the I2C bus such as generating a START condition (UCTXSTT = 1), generating a STOP condition (UCTXSTP = 1), sending an ACK (UCTXACK = 1), and sending a NACK (UCTXNACK = 1).
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 79: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.2 I2C Master Operation on the MSP430FR2355
14.3.2.1 Writing Data as an I2C Master
The easiest mode of operation is to use the Byte Counter and Automatic STOP.

## Slide 80: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.2 I2C Master Operation on the MSP430FR2355
14.3.2.1 Writing Data as an I2C Master
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
The most commonly used setting is the automatic STOP condition generation (UCASTPx).
When UCASTPx = 10, the master will automatically generate the STOP condition once the desired number of data bytes have been sent or received.
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 81: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.2 I2C Master Operation on the MSP430FR2355
14.3.2.1 Writing Data as an I2C Master
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
The last configuration needed to set up a basic master write transmission is the number of bytes that are to be sent using the UCBxTBCNT register.
The MCU will continue to send until the number of bytes transferred matches the value in UCBxTBCNT.
After the desired number of bytes has been transferred, the master will automatically generate the STOP condition if UCASTPx = 10.
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 82: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.2 I2C Master Operation on the MSP430FR2355
14.3.2.1 Writing Data as an I2C Master

## Slide 83: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.2 I2C Master Operation on the MSP430FR2355
14.3.2.1 Writing Data as an I2C Master
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
The next step is to configure the ports on the MSP430FR2355 to use the SCL and SDA.
Just as in the other serial peripherals, this is done using the PxSEL1 and PxSEL0 configuration registers.
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 84: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.2 I2C Master Operation on the MSP430FR2355

## Slide 85: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.2 I2C Master Operation on the MSP430FR2355

## Slide 86: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.2 I2C Master Operation on the MSP430FR2355
14.3.2.1 Writing Data as an I2C Master

## Slide 87: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.2 I2C Master Operation on the MSP430FR2355
UCTXIE0: After a message is Started (S), this interrupt will fire when data is ready to go into the Tx buffer.
This is used for WRITE messages.

## Slide 88: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.2 I2C Master Operation on the MSP430FR2355
UCRXIE0: After a message is Started (S), this interrupt will fire when data is ready to be ready from the Rx buffer.
This is used for READ messages.

## Slide 89: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 14: Serial Communications in C
14.3 Inter-Integrated Circuit (I2C) Bus – Master Operation on the MSP430FR2355
www.youtube.com/c/DigitalLogicProgramming_LaMeres

## Slide 90: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 14: Serial Communications in C
14.3 Inter-Integrated Circuit (I2C) Bus – Overview of the Adafruit PFC8523 Real-Time-Clock (our First I2C slave)

## Slide 91: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 14: Serial Communications in C
14.3 Inter-Integrated Circuit (I2C) Bus – Overview of the Adafruit PFC8523 Real-Time-Clock (our First I2C slave)
To begin programming the I2C peripheral on the MSP430FR2355, we need a slave that can acknowledge packets and transmit data back and forth.
We will use the PFC8523 RTC device. This is a simple I2C slave with 20x registers that can be read or written to.
The IC on this board is the NXT PCF8523 RTC + calendar (this is the datasheet we need).

## Slide 92: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 14: Serial Communications in C
14.3 Inter-Integrated Circuit (I2C) Bus – Overview of the Adafruit PFC8523 Real-Time-Clock (our First I2C slave)
www.youtube.com/c/DigitalLogicProgramming_LaMeres

## Slide 93: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 14: Serial Communications in C
14.3 Inter-Integrated Circuit (I2C) Bus – Making a Simple Probe

## Slide 94: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 14: Serial Communications in C
14.3 Inter-Integrated Circuit (I2C) Bus – Making a Simple Probe
We will be creating programs to communicate with the PCF8523 RTC via I2C.
We will need to use female-to-female jumper wires to make the connection.
When the jumpers are in place, there aren’t any pins that we can connect the AD2 to in order to do a logic analyzer measurement.
We’ll need to make a simple “probe” in order to observe the I2C messages with the AD2 logic analyzer.

## Slide 95: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 14: Serial Communications in C
14.3 Inter-Integrated Circuit (I2C) Bus – Making a Simple Probe
www.youtube.com/c/DigitalLogicProgramming_LaMeres

## Slide 96: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 14: Serial Communications in C
14.3 Inter-Integrated Circuit (I2C) Bus – Example: Writing One Byte to an I2C Slave

## Slide 97: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
Writing One Byte to an I2C Slave

## Slide 98: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
Writing One Byte to an I2C Slave

## Slide 99: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
Writing One Byte to an I2C Slave
First, put into SW Reset using the UCSWRST Bit in UCB0CTLW0.

## Slide 100: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
Writing One Byte to an I2C Slave
Next, setup clock. We’ll choose SMCLK and divide by 10 to get SCK=100kHz.

## Slide 101: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
Writing One Byte to an I2C Slave
Next we setup the I2C system:
UCMODE = I2C mode
UCMST = Master
UCTR = Transmit = Write
I2CSA = Slave Address = 0x68

## Slide 102: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
Writing One Byte to an I2C Slave
Then we setup how we’ll handle data transmission and the STOP bit.
We’ll use the Byte Counter (UCB0TBCNT) to dicate how many bytes are written.
We’ll use UCASTP=10b to automatically generate a STOP when the number of bytes in UCB0TBCNT have been sent.

## Slide 103: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
Writing One Byte to an I2C Slave
We need to use the Port Function Select (P1SEL1:P1SEL0) registers to use I2C instead of the ports.

## Slide 104: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
Writing One Byte to an I2C Slave
Next, take B0 out of SW Reset using the UCSWRST Bit in UCB0CTLW0.

## Slide 105: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
Writing One Byte to an I2C Slave
Now for triggering the message:
We’ll start a message by manually setting the UCTXSTT bit in the main loop.
We’ll use a delay loop to space out the message starts.
We’ll use a TXIFG interrupt to put data into the Tx Buffer when the message is ready (i.e., when a slave as ACK’d its slave address).

## Slide 106: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
Writing One Byte to an I2C Slave
Now for triggering the message:
We’ll start a message by manually setting the UCTXSTT bit in the main loop.
We’ll use a delay loop to space out the message starts.
We’ll use a TXIFG interrupt to put data into the Tx Buffer when the message is ready (i.e., when a slave as ACK’d its slave address).
- We’ll need to enable UCTXIE0 and write an ISR to store data to the Tx Buffer.
- The vector is: EUSCI_B0_VECTOR

## Slide 107: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
Writing One Byte to an I2C Slave
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Step 1: In CCS, create a new C/C++ Empty Project (with main.c) titled:
C_I2C_Tx1_Master_Write_1Byte
Step 2: Type in the following code in main.c after the statement to stop the watchdog timer.
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 108: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
Writing One Byte to an I2C Slave

## Slide 109: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
Writing One Byte to an I2C Slave
Step 3: Save and debug your program.
Step 4: Connect the Adafruit PCF8523 Real Time Clock to the eUSCI_B0 I2C pins on the board. You will also need to provide +3.4V and GND to the slave. All signals can be accessed on the J1 header of the board.
Step 5: Probe SCL and SCA with a logic analyzer. Configure the logic analyzer to interpret the data as an I2C bus and trigger on the START condition.
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 110: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
Writing One Byte to an I2C Slave

## Slide 111: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 14: Serial Communications in C
14.3 Inter-Integrated Circuit (I2C) Bus – Example: Writing One Byte to an I2C Slave
www.youtube.com/c/DigitalLogicProgramming_LaMeres

## Slide 112: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 14: Serial Communications in C
14.3 Inter-Integrated Circuit (I2C) Bus – Example: Writing a Register Address and Three Bytes of Data to an I2C Slave

## Slide 113: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
Writing a Register Address and Three Bytes of Data to an I2C Slave

## Slide 114: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
Writing a Register Address and Three Bytes of Data to an I2C Slave

## Slide 115: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
First, put into SW Reset using the UCSWRST Bit in UCB0CTLW0.
Writing a Register Address and Three Bytes of Data to an I2C Slave

## Slide 116: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
Next, setup clock. We’ll choose SMCLK and divide by 10 to get SCK=100kHz.
Writing a Register Address and Three Bytes of Data to an I2C Slave

## Slide 117: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
Next we setup the I2C system:
UCMODE = I2C mode
UCMST = Master
UCTR = Transmit = Write
I2CSA = Slave Address = 0x68
Writing a Register Address and Three Bytes of Data to an I2C Slave

## Slide 118: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
Then we setup how we’ll handle data transmission and the STOP bit.
We’ll use the Byte Counter (UCB0TBCNT) to dicate how many bytes are written (4).
We’ll use UCASTP=10b to automatically generate a STOP when the number of bytes in UCB0TBCNT have been sent.
Writing a Register Address and Three Bytes of Data to an I2C Slave

## Slide 119: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
Then we setup how we’ll handle data transmission and the STOP bit.
We’ll use the Byte Counter (UCB0TBCNT) to dicate how many bytes are written (4).
We’ll use UCASTP=10b to automatically generate a STOP when the number of bytes in UCB0TBCNT have been sent.
Writing a Register Address and Three Bytes of Data to an I2C Slave
We’ll create a global variable that contains an array.
The array will hold 4x bytes.
The first byte will be the register address.
The 2nd-4th will be the 3x bytes of data.

## Slide 120: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
We need to use the Port Function Select (P1SEL1:P1SEL0) registers to use I2C instead of the ports.
Writing a Register Address and Three Bytes of Data to an I2C Slave

## Slide 121: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
Next, take B0 out of SW Reset using the UCSWRST Bit in UCB0CTLW0.
Writing a Register Address and Three Bytes of Data to an I2C Slave

## Slide 122: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
Writing a Register Address and Three Bytes of Data to an I2C Slave
Now for triggering the message:
We’ll start a message by manually setting the UCTXSTT bit in the main loop.
We’ll use a delay loop to space out the message starts.
We’ll use a TXIFG interrupt to put data into the Tx Buffer when the message is ready (i.e., when a slave as ACK’d its slave address).

## Slide 123: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
- We’ll need to enable UCTXIE0 and write an ISR to store data to the Tx Buffer.
- The vector is: EUSCI_B0_VECTOR
Writing a Register Address and Three Bytes of Data to an I2C Slave
Now for triggering the message:
We’ll start a message by manually setting the UCTXSTT bit in the main loop.
We’ll use a delay loop to space out the message starts.
We’ll use a TXIFG interrupt to put data into the Tx Buffer when the message is ready (i.e., when a slave as ACK’d its slave address).

## Slide 124: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Step 1: In CCS, create a new C/C++ Empty Project (with main.c) titled:
C_I2C_Tx2_Master_Write_Reg_n_3Bytes
Step 2: Type in the following code in main.c after the statement to stop the watchdog timer.
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/
Writing A Register Address and Three Bytes of Data to an I2C Slave

## Slide 125: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
Writing A Register Address and Three Bytes of Data to an I2C Slave

## Slide 126: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
Step 3: Save and debug your program.
Step 4: Connect the Adafruit PCF8523 Real Time Clock to the eUSCI_B0 I2C pins on the board. You will also need to provide +3.4V and GND to the slave. All signals can be accessed on the J1 header of the board.
Step 5: Probe SCL and SCA with a logic analyzer. Configure the logic analyzer to interpret the data as an I2C bus and trigger on the START condition.
Writing A Register Address and Three Bytes of Data to an I2C Slave
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 127: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
Writing A Register Address and Three Bytes of Data to an I2C Slave

## Slide 128: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 14: Serial Communications in C
14.3 Inter-Integrated Circuit (I2C) Bus – Example: Writing a Register Address and Three Bytes of Data to an I2C Slave
www.youtube.com/c/DigitalLogicProgramming_LaMeres

## Slide 129: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 14: Serial Communications in C
14.3 Inter-Integrated Circuit (I2C) Bus – Example: Reading One Byte from an I2C Slave

## Slide 130: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.2 I2C Master Operation on the MSP430FR2355
14.3.2.2 Reading Data as an I2C Master
The only difference during eUSCI_B0 initialization for reading is to put the peripheral into receive mode using UCTR = 0.
The UCRXIFG0 will be asserted when the slave sends back a byte of data and it arrives in the Rx buffer.
This flag will trigger an eUSCI_B0 interrupt.
The Rx buffer value will be stored in a variable.
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 131: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.2 I2C Master Operation on the MSP430FR2355
14.3.2.2 Reading Data as an I2C Master
The master will produce a NACK signal after the last byte in the transmission has been received as dictated by the value in UC0TBCNT.
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 132: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
Reading One Byte From an I2C Slave

## Slide 133: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
Reading One Byte From an I2C Slave

## Slide 134: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
Reading One Byte From an I2C Slave
First, put into SW Reset using the UCSWRST Bit in UCB0CTLW0.

## Slide 135: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
Reading One Byte From an I2C Slave
Next, setup clock. We’ll choose SMCLK and divide by 10 to get SCK=100kHz.

## Slide 136: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
Reading One Byte From an I2C Slave
Next we setup the I2C system:
UCMODE = I2C mode
UCMST = Master
UCTR = Receive = Read
I2CSA = Slave Address = 0x68

## Slide 137: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
Reading One Byte From an I2C Slave
Then we setup how we’ll handle data transmission and the STOP bit.
We’ll use the Byte Counter (UCB0TBCNT) to dicate how many bytes are read.
We’ll use UCASTP=10b to automatically generate a STOP when the number of bytes in UCB0TBCNT have been received.

## Slide 138: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
Reading One Byte From an I2C Slave
We need to use the Port Function Select (P1SEL1:P1SEL0) registers to use I2C instead of the ports.

## Slide 139: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
Reading One Byte From an I2C Slave
Next, take B0 out of SW Reset using the UCSWRST Bit in UCB0CTLW0.

## Slide 140: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
Reading One Byte From an I2C Slave
Now for triggering the message:
We’ll start a message by manually setting the UCTXSTT bit in the main loop.
We’ll use a delay loop to space out the message starts.
We’ll use a RXIFG interrupt to read data out of the Rx Buffer after it arrives.

## Slide 141: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
Reading One Byte From an I2C Slave
- We’ll need to enable UCRXIE0 and write an ISR to read the Rx buffer.
- The vector is: EUSCI_B0_VECTOR
Now for triggering the message:
We’ll start a message by manually setting the UCTXSTT bit in the main loop.
We’ll use a delay loop to space out the message starts.
We’ll use a RXIFG interrupt to read data out of the Rx Buffer after it arrives.

## Slide 142: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Step 1: In CCS, create a new C/C++ Empty Project (with main.c) titled:
C_I2C_Rx1_Master_Write_1Bytes
Step 2: Type in the following code in main.c after the statement to stop the watchdog timer.
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of
Recording Connection of Canada
Image Courtesy of https://neodem.wp.horizon.ac.uk/
Reading One Byte From an I2C Slave

## Slide 143: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
Reading One Byte From an I2C Slave

## Slide 144: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
Step 3: Save and debug your program.
Step 4: Connect the Adafruit PCF8523 Real Time Clock to the eUSCI_B0 I2C pins on the board. You will also need to provide +3.4V and GND to the slave. All signals can be accessed on the J1 header of the board.
Step 5: Probe SCL and SCA with a logic analyzer. Configure the logic analyzer to interpret the data as an I2C bus and trigger on the START condition.
Reading One Byte From an I2C Slave
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 145: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
Reading One Byte From an I2C Slave

## Slide 146: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 14: Serial Communications in C
14.3 Inter-Integrated Circuit (I2C) Bus – Example: Reading One Byte from an I2C Slave
www.youtube.com/c/DigitalLogicProgramming_LaMeres

## Slide 147: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 14: Serial Communications in C
14.3 Inter-Integrated Circuit (I2C) Bus – Example: Reading From a Specific Slave Register Address Using Two I2C Messages

## Slide 148: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
Reading From a Specific Slave Register Address Using Two I2C Messages

## Slide 149: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
Reading From a Specific Slave Register Address Using Two I2C Messages

## Slide 150: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
First, put into SW Reset using the UCSWRST Bit in UCB0CTLW0.
Reading From a Specific Slave Register Address Using Two I2C Messages

## Slide 151: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
Next, setup clock. We’ll choose SMCLK and divide by 10 to get SCK=100kHz.
Reading From a Specific Slave Register Address Using Two I2C Messages

## Slide 152: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
Next we setup the I2C system:
UCMODE = I2C mode
UCMST = Master
UCTR = “leave for now”
I2CSA = Slave Address = 0x68
Reading From a Specific Slave Register Address Using Two I2C Messages

## Slide 153: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
Reading From a Specific Slave Register Address Using Two I2C Messages
Then we setup how we’ll handle data transmission and the STOP bit.
We’ll use the Byte Counter (UCB0TBCNT) to dicate how many bytes are read.
We’ll use UCASTP=10b to automatically generate a STOP when the number of bytes in UCB0TBCNT have been received.

## Slide 154: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
We need to use the Port Function Select (P1SEL1:P1SEL0) registers to use I2C instead of the ports.
Reading From a Specific Slave Register Address Using Two I2C Messages

## Slide 155: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
Next, take B0 out of SW Reset using the UCSWRST Bit in UCB0CTLW0.
Reading From a Specific Slave Register Address Using Two I2C Messages

## Slide 156: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
Reading From a Specific Slave Register Address Using Two I2C Messages
Now for triggering the message:
We’ll start the two messages manually in the main loop by setting the UCTXSTT bit in the main loop.
We’ll use delay loops to space out the message starts.
We’ll use TXIFG & RXIFG interrupts to send the registers address and then read the Rx Buffer.

## Slide 157: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
- We’ll need to enable UCTXIE0 & UCRXIE0 and write an ISR to write the Tx buffer and read the Rx buffer.
- The vector is: EUSCI_B0_VECTOR.
- Let’s use UCB0IV (1st time)
Reading From a Specific Slave Register Address Using Two I2C Messages
Now for triggering the message:
We’ll start the two messages manually in the main loop by setting the UCTXSTT bit in the main loop.
We’ll use delay loops to space out the message starts.
We’ll use TXIFG & RXIFG interrupts to send the registers address and then read the Rx Buffer.

## Slide 158: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
Step 1: In CCS, create a new C/C++ Empty Project (with main.c) titled:
C_I2C_Rx2_Master_Read_From_Reg_Addr
Step 2: Type in the following code in main.c after the statement to stop the watchdog timer.
Image Courtesy of https://neodem.wp.horizon.ac.uk/
Reading From a Specific Slave Register Address Using Two I2C Messages

## Slide 159: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
Reading From a Specific Slave Register Address Using Two I2C Messages

## Slide 160: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
Reading From a Specific Slave Register Address Using Two I2C Messages

## Slide 161: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
Step 3: Save and debug your program.
Step 4: Connect the Adafruit PCF8523 Real Time Clock to the eUSCI_B0 I2C pins on the board. You will also need to provide +3.4V and GND to the slave. All signals can be accessed on the J1 header of the board.
Step 5: Probe SCL and SCA with a logic analyzer. Configure the logic analyzer to interpret the data as an I2C bus and trigger on the slave address of 0x68.
Reading From a Specific Slave Register Address Using Two I2C Messages
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 162: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
Reading From a Specific Slave Register Address Using Two I2C Messages

## Slide 163: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 14: Serial Communications in C
14.3 Inter-Integrated Circuit (I2C) Bus – Example: Reading From a Specific Slave Register Address Using Two I2C Messages
www.youtube.com/c/DigitalLogicProgramming_LaMeres

## Slide 164: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 14: Serial Communications in C
14.3 Inter-Integrated Circuit (I2C) Bus – Slave Operation on the MSP430FR2355

## Slide 165: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.3 I2C Slave Operation on the MSP430FR2355
While most of the time an MCU acts as the I2C master, the MSP430FR2355 also can be configured as an I2C slave.
Use UCMODx = 11 puts the peripheral into I2C mode.
Use UCMST = 0 configures the peripheral as a slave.
Image Courtesy of https://neodem.wp.horizon.ac.uk/

## Slide 166: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.3 I2C Slave Operation on the MSP430FR2355
In slave mode, the MCU doesn’t produce SCL, so no configuration of UCSSELx or UCBRx is needed.

## Slide 167: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.3 I2C Slave Operation on the MSP430FR2355
The MSP430 supports up to four separate and user-programmable slave addresses.
The slave address values are stored in the eUSCI_Bx I2C Own Address n (UCBxI2COAn) registers by the user during initialization.

## Slide 168: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.3 I2C Slave Operation on the MSP430FR2355
The four specific register names in the MSP430 are UCBxI2COA3, UCBxI2COA2, UCBxI2COA1, UCBxI2COA0.

## Slide 169: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.3 I2C Slave Operation on the MSP430FR2355
The MCU is first put into receiver mode using UCTR = 0 in order to receive the I2C slave address that the master sends out to all slaves.

## Slide 170: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.3 I2C Slave Operation on the MSP430FR2355
Each register contains an Own Address Enable (UCOAEN) bit in position 10 that must be asserted if the slave address is to be active.

## Slide 171: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.3 I2C Slave Operation on the MSP430FR2355
The UCBxI2CA0 register is unique in that its 15th position is the General Call Response Enable (ECGEN) for the MCU’s entire slave system.

## Slide 172: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.3 I2C Slave Operation on the MSP430FR2355
The 15th position in the other three I2C own address registers are reserved.

## Slide 173: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.3 I2C Slave Operation on the MSP430FR2355
Each slave address contains independent interrupt flags for both Tx and Rx.

## Slide 174: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.3 I2C Slave Operation on the MSP430FR2355
If the I2C slave address sent by a master matches any of the values in an enabled UCBxI2COAn register, an ACK will be automatically sent and the UCSTTIFG flag is set.

## Slide 175: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.3 I2C Slave Operation on the MSP430FR2355
If the I2C slave address sent by a master matches any of the values in an enabled UCBxI2COAn register, an ACK will be automatically sent and the UCSTTIFG flag is set.
Whether the MCU is supposed to transmit or receive is configured automatically by setting the corresponding UCTXIFG or UCRXIFG flag in the slave.

## Slide 176: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.3 I2C Slave Operation on the MSP430FR2355
The user needs to read or write to the Tx or Rx buffers within the eUSCI_B service routine depending on the type of data transfer that is being requested.

## Slide 177: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.3 I2C Slave Operation on the MSP430FR2355
For a slave transmit, data is put into the Tx buffer and automatically shifted out.
This ACK will trigger another transmit interrupt so that the MCU can send more data.
If the master is done receiving data, it will send a NACK followed by the STOP condition to end the message.

## Slide 178: Ch. 14: Serial Communication in C
14.3 Inter-Integrated Circuit (I2C) Bus
14.3.3 I2C Slave Operation on the MSP430FR2355
For a slave receive, the master will shift data into the Rx shift register.
When complete, the data will be transferred to the Rx buffer and the UCRXIFG is asserted indicating that it’s ready to be transferred inot an internal variable.
The slave will then send an ACK signal back to the master.

## Slide 179: Embedded Systems Design
Brock J. LaMeres, Ph.D.
Chapter 14: Serial Communications in C
14.3 Inter-Integrated Circuit (I2C) Bus – Slave Operation on the MSP430FR2355
www.youtube.com/c/DigitalLogicProgramming_LaMeres